SQC Sprayer Maintenance and Self Assessment form (complete annually if sprayer not NSTS tested)

Calibration Record

Calibration

Must be carried out regularly at the beginning of each spray season, (spring and autumn), and regularly during the season and always after changing tractor, tractor wheels, nozzles or replacing any part of the spray delivery system.

When calibrating the sprayer, wear a minimum of a coverall, gloves and boots:

|  |  | Enter Values |
| --- | --- | --- |
| Read the LABEL | Spray VOLUME Spray DOSE Spray QUALITY |  |
| Measure TIME per 100m | Measure time in seconds over land similar to that to be sprayed |  |
| Calculate SPEED | Speed = 360 ÷ Time (seconds) |  |
| Measure nozzle SPACING on boom | (normally 0.5m) |  |
| Calculate nozzle OUTPUT | Output = Volume x speed x space ÷ 600 (Litres/min) (litres/ha) (km/h) (metre) |  |
| Select NOZZLE | Refer to nozzle manufacturers chart and select size and type of nozzle that will produce the calculated OUTPUT and required spray QUALITY |  |

Now check the calibration of the sprayer:

| Check Nozzle OUTPUT | Using water, check output of 4 or more nozzles using a calibration jug or flow meter. |  |
| --- | --- | --- |
| Calibrate SPRAYER | Volume = output x 600 ÷ space ÷ speed (Litres/ha) (litres/min) (metre) (km/h) |  |

Record Details					                       Date Completed: ______________

| Nozzles fitted |  | Tractor used |  |
| --- | --- | --- | --- |
| Spray volume |  | Tractor gear |  |
| Spray pressure |  | Tractor wheels |  |
| Spray quality |  | Tractor revs |  |
| Forward speed |  |  |  |

Further forms can be downloaded from the SQC Website www.sqcrops.co.uk or obtained by telephoning the SFQC office: 0131 335 6604

This form is reproduced with kind permission of the BCPC

# Text boxes

Owner:					Operator:				Make:

Model:					PA Cert no:				Reg No:

Date:					NRoSO no:

Key:		Checked/Completed     (			Needs Attention	       X

Adjusted		A			Not Applicable	      na

Regularly (cont)

##### Controls and valves

- Are the master on/off switches working correctly?

- Are all boom section switches functioning?

- Can you read the pressure gauges easily?

- Are all labels appropriate and legible?

- Is the pressure adjustment/stable?

- Pressure gauge reading zero?

##### Chemical induction system

- Are the system and controls working properly?

- Is it free from leaks under pressure?

- Are all labels appropriate and readable?

- Is the rinse system and container wash system working properly?

##### Tank rinse system

- Is the system functioning properly?

##### External washdown

- Is the system functioning properly?

##### Personal

- Water supply tank filled?

- Is the clothing locker clean and contents complete?

Periodical

#### Jug test all nozzle outputs

Date Completed ………………………….

- Formally complete and file check sheet

Independent test due (if applicable)……………………

Maintenance Required/Completed/Specific items requiring attention

Regularly

# Mechanical

- Is the attachment to tractor secure?

- Is the chassis and structure free of cracks and rust?

- Are the wheels and tyres in good condition?

- Are guards, inc. PTO shaft guard, secure and undamaged?

## Hydraulic system, inc. tracking system if fitted.

## Are they free from leaks under pressure?

## Are the hoses and connections worn or cracked?

## Electrical system

## Is the wiring undamaged & are all connections properly insulated?

## Do all the lights work properly?

## Pneumatic system

## Is the system free from leaks when under working under operating pressures?

## Sprayer tank

## Are the tank/chassis fasteners secure?

## Free from leaks?

## Does the lid fit securely and free from leaks?

## Is the contents gauge clearly legible?

## Boom

## Is it properly latched when folded for transport?

## When unfolded, is it straight and level?

- Does the height adjustment and suspension work properly?

- Does the boom return to level when displaced to left and right?

- Are the break-backs functioning freely?

- Are the mountings and linkages secure and not worn?

### 'Spray lines'

- Are they free from leaks under pressure?

- No hoses and connectors worn or cracked?

- Are all valves and filters in good condition?

### Nozzles

- Are all fittings and turrets in good condition?

- Are all nozzles correctly orientated?

- Are all check valves working properly?

- Is the spray/distribution pattern visually correct?